- CONFIGURATION

Given the physical topology below, state the proper syntax needed to configure the routers and the computers included in the topology.

Sample Configuration:

router#config t

router(config)#int fa0/0

router(config-if)#ip add 192.22.3.1 255.255.255.0

router(config-if)#no shut

***Refer to Network Address Assignment table below.

- Configuration of host devices (fill the table below with the appropriate details)

|  | Host IP Address | Subnet Mask | Default Gateway |
| --- | --- | --- | --- |
| PC0 |  |  |  |
| PC1 |  |  |  |
| PC2 |  |  |  |
| PC3 |  |  |  |

- Configuration of R0 interfaces (2 interfaces)

- Configuration of R1 interfaces (2 interfaces)

- Configuration of R2 interfaces (3 interfaces)

***NETWORK ADDRESS ASSIGNMENT TABLE

| STUDENT | NETWORK A | NETWORK B | NETWORK C | NETWORK D |
| --- | --- | --- | --- | --- |
| Borje | 19.128.0.0/9 | 200.100.16.0/30 | 192.201.128.128/30 | 192.168.1.0/24 |
| Brigino | 19.128.0.0/12 | 38.177.8.0/30 | 192.201.64.128/30 | 192.168.2.0/24 |
| Carreon | 19.128.0.0/11 | 200.100.16.0/29 | 192.201.8.128/30 | 192.168.3.0/24 |
| Collantes | 19.128.0.0/12 | 38.177.8.0/29 | 192.201.16.128/30 | 192.168.4.0/24 |
| Gaddi | 19.128.0.0/13 | 200.100.16.0/28 | 192.201.4.128/30 | 192.168.5.0/24 |
| Guillema | 19.128.0.0/14 | 38.177.8.0/28 | 192.201.68.128/30 | 192.168.6.0/24 |
| Julian | 19.128.0.0/15 | 200.100.16.0/27 | 192.201.132.128/30 | 192.168.7.0/24 |
| Llorera | 19.128.0.0/17 | 38.177.8.0/27 | 192.201.192.128/30 | 192.168.8.0/24 |
| Luat | 19.128.0.0/18 | 200.100.16.0/26 | 192.201.228.128/30 | 192.168.9.0/24 |
| Martin | 19.128.0.0/19 | 38.177.8.0/26 | 192.201.196.128/30 | 192.168.10.0/24 |
| Monteveros | 19.128.0.0/20 | 200.100.16.0/25 | 192.201.24.128/30 | 192.168.11.0/24 |
| Nabus | 19.128.0.0/21 | 38.177.8.0/25 | 192.201.28.128/30 | 192.168.12.0/24 |
| Nepomuceno | 19.128.0.0/22 | 200.100.16.0/24 | 192.201.20.128/30 | 192.168.13.0/24 |
| Palomar | 19.128.0.0/23 | 38.177.8.0/24 | 192.201.36.128/30 | 192.168.14.0/24 |
| Perono | 19.128.0.0/25 | 200.100.16.0/23 | 192.201.48.128/30 | 192.168.15.0/24 |
| Pertubal | 19.128.0.0/26 | 38.177.8.0/23 | 192.201.144.128/30 | 192.168.16.0/24 |
| Ronquillo | 19.128.0.0/27 | 200.100.16.0/22 | 192.201.80.128/30 | 192.168.17.0/24 |
| Santiago | 19.128.0.0/28 | 38.177.8.0/22 | 192.201.100.128/30 | 192.168.18.0/24 |
| Senosa | 19.0.0.0/7 | 200.100.16.0/21 | 192.201.52.128/30 | 192.168.19.0/24 |
| Wong | 19.0.0.0/6 | 38.177.8.0/21 | 192.201.12.128/30 | 192.168.20.0/24 |