Air from inside a house enters a steady-flow heat exchanger with a volume flow rate of 200 m3/min at 15°C, 100kPa and eaves the heat exchanger at 35°C.  This heat exchanger is located inside the sir handler of a house heat pump systemand receives heat from the heat pump.  The heat pump receives heat from air outside the house that acts as a heat source at 10°C.

Assume air has constant specific heats evaluated at 300K.

- Determine the heat supplied to the sir in the heat exchanger Q.  H, in kW.

- Assuming the air in the heat exchanger acts as a heat sink having an average temperature of 25°C, determine the minimum power supplied to the heat pump, in kW.

# Text boxes

Air inlet

Heat Exchanger

Air

Exit

Work

Input

Outside Air Heat

Source, 10°C

QH

QL

HP