# Product-Mix Information
Prepared by the Marketing Department

Professor Tillerman's Tonic Tea produces its three blends in the manner outlined below. Since their introduction, the two new flavors have been extremely popular with customers (especially the Kyoto Blend), and account for 85 percent of our current production.

# Current Marketing Data

|  | Kyoto Blend | Beijing Blend | New Delhi Blend |
| --- | --- | --- | --- |
| Profit Margins ($ per case) | $3.05 | $3.51 | $3.11 |
| Current Product Mix* | 60% | 15% | 25% |

* The current product-mix data apply to the Chicago facility (and all Tillerman's Tea brewing facilities).

# Production Process
Presented by Leif Stewart, brewmaster

The production process at Professor Tillerman's Tonic Tea is within industry standards and is based on recommended specifications from our suppliers.

## Manufacturing Times

|  | Operation (Machine Hours per 100 Cases) |
| --- | --- |
| Blend | Brewing | Filtration | Finishing | Bottling |
| Kyoto | 0.8141 | 0.7739 | 0.7438 | 1.62827 |
| Beijing | 0.9146 | 0.7639 | 0.8744 | 1.62827 |
| New Delhi | 0.7136 | 0.9046 | 0.8242 | 1.62827 |

## Capacity Information

Brewing, filtration, and finishing are batch operations. In the Chicago plant, there is one machine each for brewing, filtration, and finishing; for the bottling operation two machines run simultaneously.

| Operation | No. of Machines | Total Capacity per Week |
| --- | --- | --- |
| Brewing | 1 | 96 hours |
| Filtration | 1 | 96 hours |
| Finishing | 1 | 96 hours |
| Bottling | 2 | 192 hours |

## Floor Plan of a Typical Tillerman's Tea Brewing Facility