a)	Predetermined…

$830,000 ÷ 100,000 hrs.  = $8.30 per machine hour

(b)	Manufacturing cost per stair under traditional costing:

Direct materials		$103,600

Direct labor		 112,000

Overhead (14,500 X $8.30)		 120,350

Total cost of 280 stairs		$335,950

Cost per stair ($335,950 ÷ 280)		 $1,199.82

(c)	Manufacturing cost per stair under activity-based costing:

Computation of Activity-Based Overhead Rate

|  | Activity Cost Pool |  | Estimated Overhead | ÷ | Total Estimated Drivers | = | Activity-Based Overhead Rate |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | Purchasing Handling materials Production Setting up machines Inspecting Inventory control Utilities |  | $ 57,000 82,000 210,000 85,000 90,000 126,000 180,000 $ 830,000 |  | 600 Orders 8,000 Moves 100,000 D/L Hours 1,250 Setups 6,000 Inspections 168,000 Components 90,000 Sq. ft. |  | $95.00 per order $10.25 per move $2.10 per D/L hour $68.00 per setup $15.00 per inspection $.75 per component $2.00 per sq. ft. |

Assignment of Overhead to Order of 280 Stairs

|  | Activity Cost Pool |  | Expected Use of Driver | X | Activity-Based Overhead Rate | = | Cost Assigned |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | Purchasing Handling materials Production Setting up machines Inspecting Inventory control Utilities |  | 60 Orders 800 Moves 5,000 D/L Hours 100 Setups 450 Inspections 16,000 Components 8,000 Sq. ft. |  | $95.00 $10.25 $2.10 $68.00 $15.00 $.75 $2.00 |  | $ 5,700 8,200 10,500 6,800 6,750 12,000 16,000 |
|  | Total overhead assigned |  |  |  | $65,950 |

Chapter 4 Problem 4-3A (Continued)

Total manufacturing cost per stair under ABC:

Direct materials		$  103,600

Direct labor		112,000

Overhead		  65,950

Total cost of 280 stairs		$  281,550

Total cost per stair (281,550/280)		$1,005.54

(d)	The difference between the traditional cost and the activity-based cost per unit of $194.28 or ($1,005.54 vs. $1,199.82) is not great in amount but—xx.3%…