4) A power plant burns 104 kg hr-1 of coal that contains 2.5% sulfur. The stack is 50 m high, and the plume typically rises 30 m.

a) Calculate the ground-level concentration of SO2 (in (g m-3) 800 m downwind from the source directly under the plume under the following conditions: Wind speed = 4 m s-1, moderately sunny day (moderately unstable conditions).

b) Repeat the above calculation for a stack height of 75 m and a wind speed of 6 m s-1.

|  |  |  | Surface | Wind | Speed |  |
| --- | --- | --- | --- | --- | --- | --- |
| Insolation | Cloud cover | <2 | 2 to 3 | 3 to 5 | 5 to 6 | >6 |
|  | Strong sun | A | A-B | B | C | C |
| Day | Mod. Sun | A-B | B | B-C | C-D | D |
|  | Slight sun | B | C | C | D | D |
| Day or | Overcast | D | D | D | D | D |
| Night |  |  |  |  |  |  |
| Night | ≥ 0.5 cloud cover |  | E | D | D | D |
|  | ≤ 0.4 cloud cover |  | F | E | D | D |