Activity 1

(a). Generate a random input signal x(t) in MATLAB by using the

command rand. In particular, let x = rand(1000,1)-0.5. This will

create a 1000 point vector of random numbers that represents the

samples of x(t). Assume that the sampling period was T = 0.1, and

create a corresponding time vector.

(b). Use MATLAB to determine a corresponding output y(t) for a particular

system. In particular, type the command y=conv(exp(-t),x); to generate

y(t). The array y will be 1999 elements long by virtue of how the

convolution works. Use only the first 1000 elements. Plot x versus t

and y versus t, and compare the two signals in terms of frequency

content.

(c). Suppose that you have a spectrum analyzer available to identify the

system using only the signals x(t) and y(t). Use contfft to compute the

approximation X to X(w) and an approximation of Y to Y(w). Plot

|X(w)| and |Y(w)| versus w ,  and compare the difference in frequency

content of these two signals. The frequency vector provided by the

contfft command ranges from 0 to 62.769 rad/sec. However, since the

sampling period is 0.1 sec, the Nyquist frequency is pi/T, 31.4159

rad/sec.  We only need the frequencies from 0 to the Nyquist frequency, so only consider

the plot in the range of 0 ≤w≤30 rad/sec.

(d). Recall that Y(w) = X(w)H(w). Compute the approximation to H(w) by

dividing the elements of Y by the elements of X. Plot the frequency

response |H(w)|.

Questions:

What sort of filter does this represent? What is its bandwidth?

Contfft Program

function [X,w] = contfft(x,T);

% CONTFFT [X,w] = contfft(x,T)

%

% Computes the Fourier transform of a continuous time signal

% using the FFT. The input is the sampled continuous

% time signal x and the sampling time T. The output is

% the Fourier transform X(w) and the frequency vector w.

%

[n,m] = size(x);

if n<m,

x = x';

end

Xn = fft(x);

N = length(x);

n = 0:N-1;

n(1) = eps;

X = (1-exp(-j*2*pi*n/N))./(j*2*pi*n/N/T).*Xn.';

w = 2*pi*n/N/T;