A spacer defines the air-gap distance between a lens and a flat surface.  The corner of the spacer can be modeled as a circle with radius, r1.   First a circular lens is used, and the “sag,” or amount that the lens bulges out on the axis, defines the air gap distance by: sag = R – (R2 – (chord)2) ½

In this case the contact point Δy above the axis is pretty straight forward to find.  If now the lens is replaced with an asphere, sag defined as “z” below

Z =sag height
r =radial distance from vertex (Chord, or “half-chord”)
c= (1/R) = curvature at the vertex 
K=conic constant

Find the correction to the 1st order in r in the relation between Δy and H, where H is the difference between the full width of the spacer and the air gap

# Text boxes

r

R

Δy

r1

Sag distance

Flat surface

spacer

Axis

chord

Air gap