Questions 1 - 5: Problem 9-34; Note that the selection must be made based on incremental B/C analysis.

Questions 9 - 16: Problem 9-50.

1. The benefit cost ratio for alternative A can be calculated with which equation? B/C = [ 140 (P/A,i,6) + 40 (P/F,I,6) ]/ [ 560 ] B/C = [ 140 (P/A,i,6) ]/ [ 560 + 40(P/F,i,6)] B/C = [ 140 (P/A,i,6) - 40 ]/ [ 560 ] B/C = [ 140 (P/A,i,6) ] / [ 560 – 40(P/F,i,6)] 2. The benefit cost ratio for alternative C is most nearly 1.18 1.29 1.45 1.51 3. The incremental benefit cost ratio for (B-C) is most nearly -0.17 0.44 0.86 1.19 4. The incremental benefit cost ratio for (A-B) is most nearly -0.15 0.18 0.88 1.57 5. Which alternative is preferred? A B C 6. Problem 9-2 F is proportional to x. The equation is F = ax. The numerical value of a is most nearly 11 12 13 15 7. Problem 9-64 The value of X is most nearly 140 260 290 300 8. Problem 9-68 This problem can be approached by determining EUAC. At the breakeven point, which defines the value of the maximum treatment cost, EUACtreated = EUACuntreated. 1.60 2.50 2.70 2.90 9. Using the 12 year analysis period (which is the correct procedure), the Net Future Worths of A,B, and C, respectively are most nearly -18.9, 75.2, 86.6 20.3, -14.4, 46.1 -22.9, 75.2, 46.1 -18.9, 75.2, 63.3 10. Based on Future Worth Analysis, the recommended alternative is A B C 11. The Payback Period (years) for A is most nearly 0.56 0.72 1.13 1.74 12. The Payback Period (years) for B is most nearly 2.4 2.6 3.1 3.8 13. Based on Payback Period, the preferred alternative is A B C 14. The incremental B/C for (C-A) is most nearly 0.72 0.95 1.21 1.51 15. The incremental B/C for (B-C) is most nearly 0.72 0.99 1.21 1.51 16. Based on Incremental B/C Analysis, the preferred alternative is A B C