CASE:  GOLDEN KERNEL PROCESSING COMPANY

Delana Lightfoot is a production analyst at the Golden Kernel processing plant, which processes whole-kernel cut corn.  Delana’s current project is to evaluate different levels of automation for quality control inspection of corn kernels.  Option 1 is to assign a number of employees along the conveyor belt to inspect the corn kernels manually as they go by and pick out small and off-color kernels.  Option 2 involves using fewer employees who only check for off-color kernels and then running the corn over a screen that filters out the small kernels.  Option 3 is to purchase a state-of-the-art, fully automated machine that uses video cameras, a computer workstation, and small bursts of air.  This new machine can automatically inspect individual kernels of corn for size and color as the conveyer belt moves the kernels in a single layer by the machine.  Inferior kernels are removed by a precisely placed small burst of air as the kernels pass over a perforated air tube.

As Delana expected, the initial costs of the options vary substantially.  She investigated the cost of each option and has summarized the information in the following table:

OPTION 1		OPTION 2		OPTION 3

Annual Fixed Cost		$2,500			$4,500			$27,000

Variable cost per 		100			80			20

thousand pounds

Assignment

- Based on annual cost, determine the annual volume (in thousands of pounds) at which the company would be indifferent between Option 1 and Option 2; between Option 2 and Option 3; and between Option 1 and Option 3.

- Create a table showing the total annual cost of each option if annual volume (in thousands of pounds) is 50, 200, 350, and 500.  Circle the lowest cost at each annual volume.

- Based only on annual cost, for what range of annual volumes would each option be preferred?

- What factors other than annual cost should be considered when making this decision?