Performance tests of a DC motor under load conditions.

Test 1

| Load (%) | 10 | 20 | 30 | 40 | 50 |
| --- | --- | --- | --- | --- | --- |
| Force | 0.6 | 1.1 | 2 | 2.5 | 3 |
| Armature Current | 0.85 | 1.38 | 1.98 | 2.5 | 2.9 |
| Armature Voltage | 25 | 25 | 25 | 25 | 25 |
| Speed (rpm) | 1420 | 1220 | 1000 | 840 | 720 |

Assuming that the basic equations of the motor are

Va = Ra Ia +K1 n     and   Te = To + K2 Ia

Using the data above, estimate the coefficients Ra, K1, T0 and K2