The Bench Company is a small manufacturer of wooden benches. Their line includes four types of benches that differ in size, material, finish, and color. Pertinent production data are as follows:

Bench Type

1		2		3		4

Annual Demand (units)	1000		5000		10,000		8000

Set-up cost ($)		6		10		10		8

Unit cost ($)			10		3		5		2

Space per unit (ft2)		5		1		1		1

Bench has a small warehouse for finished benches, which has an area of 1500 ft2. Each bench has affixed location. Assuming i=20 percent annually, calculate the optimal quantities to be stored.

Bench has an offer to double the storage space, which will result in an increase of $200 in annual expenses. Should bench do it?