#1) A system whose equation of state depends only on pressure P, volume V and temperature T is taken quasi-statically from state from state A to state B (in the figure shown above) along path ACB at the pressures indicated. In this process 50J of heat enter the system and 20J of work are done by the system.

- how much heat enters the system along path ADB?

- If the system goes from B to A along the curved path indicated on the diagram (imagine this is a smooth curve) the work done on the system is 25J how much heat enters or leaves the system?

- If the internal energy at A is denoted by UA   and the internal energy at B by UB and so on around the path Suppose that UD - UA = 25J. What then is the heat transfer involved in the process AD to DB

#2) 10 ^-3 m^3 of lead is compressed reversibly and isothermally at room temperture from 1 to 1000 atms. Pressure.

- How much work is done on the lead? The isothermal compressibility of lead is 2.2 x10^-6 (atm)^-1  (this is assumed independent of pressure).Use 1 atm~10^5 pa

- What is the change in the internal energy of the lead if the amount of lead is compressed reversibly but adiabatically from 1 to 1000atm.

# Text boxes

A

C

D

B

P

V

5P1

P1