The following tasks, which cannot be split, must be performed on an assembly line in the sequence and the times specified. The required cycle time is 75 seconds.

| Task | Task time (Sec.) | Immediate predecessor |
| --- | --- | --- |
| A | 50 | NONE |
| B | 40 | NONE |
| C | 20 | A |
| D | 45 | C |
| E | 20 | C |
| F | 25 | D |
| G | 15 | E |
| H | 35 | B,F,G, |
|  | 250 |  |

- Draw precedence diagram.

- Balance this line using the largest number of following tasks as the primary rule, and longest task time as the tie-breaker. What is the correct assignment of tasks to stations? (You will not necessarily use all of the stations listed, but you will definitely not need more than 5 stations.)

Station I           Station II            Station III             Station IV             Station V