2.3

A four-bar straight-line mechanism is shown in figure 2.42. For specified values of the input link length r and the input angle , the coupler angle  and the follower angle  can be computed by solving the following vector loop equations:

rcos + rcos - rcos - r = 0

and

rsin + rsin - rsin = 0.				(E1)

The x and y components of the position of the coupler point P can be determined as

x =  rcos + rcos

and

y =  rsin + rsin				(E2)

Solve Eqs. (E1) using Newton-Raphson method, find the (x, y) coordinates of P using Eqs. (E2), and plot the position of P for the following data:

r= 0.963, r= 0.764, r= 0.528, r= 1.815,

r= 0.778,  = -0.89.65, and .