- Use the results in Table Q2. from a tensile test on 70/30 brass, to:

- Draw the load vs extension graph;

- Determine the Modulus of Elasticity;

- Determine the 0.1% proof stress.

TABLE Q2

Test Results for 70/30 As Drawn Brass

Test Piece:	Gauge Length	50mm

Cross Section Area, 	20 mm2

| LOAD (Kn). | EXTENSION (mm) |
| --- | --- |
| 1 | 0.02 |
| 2 | 0.044 |
| 3 | 0.067 |
| 4 | 0.091 |
| 5 | 0.136 |
| 5.5 | 0.196 |
| 6 | 0.4 |