- Design a digital LPF to be used in the configuration

H(z) is the digital low-pass filter.

To satisfy the following requirements:

- Sampling rate = 8 kilosamples/sec

- Passband edge of 1.5kHz with ripple of 3dB

- Stopband edge of 2kHz with attenuation of 40dB

- Equiripple Passband but monotone Stopband, and

- Impulse invariance

  - Choose T=1 in the impulse invariance method and determine the system function H(z) in parallel form. Plot the log-magnitude response in dB and the impulse response h(n).

  - Choose T=1/8000 in the impulse invariance method and determine the system function H(z) in parallel form. Plot the log-magnitude response in dB and the impulse response h(n). Comment on the effect of T on the impulse invariance.