Golden Kernel Processing Company 1

Delana Lighfoot is a production analyst at the Golden Kernel processing plant, which processes whole-kernel cut corn. Delana’s current project is to evaluate different levels of automation for quality control inspection of corn kernels.

Option 1 is to assign a number of employees along the conveyor belt to inspect the corn kernels manually as they go by and pick out small and off-color kernels.

Option 2 involves using fewer employees who only check for off-color kernels and then running the corn over a screen that filters out the small kernels.

Option 3 is to purchase a state-of-the-art, fully automated machine that uses video cameras, a computer workstation, and small bursts of air. This new machine can automatically inspect individual kernels of corn for size and color as the conveyer belt moves the kernels in a single layer by the machine. Inferior kernels are removed by a precisely placed small burst of air as the kernels pass over a perforated air tube.

As Delana expected, the initial costs of the options vary substantially. She investigated the cost of each option and has summarized the information in the following table:

|  | Option 1 | Option 2 | Option 3 |
| --- | --- | --- | --- |
| Annual fixed cost | 2,500 | 4,500 | 27,000 |
| Variable cost per | 100 | 80 | 20 |
| Thousand pounds |  |  |  |

- Based on annual cost, determine the annual volume (in thousands of pounds) at which the company would be indifferent between Option 1 and Option 2; between Option 2 and Option 3; and between Option 1 and Option 3.

- Create a table showing the total annual cost of each option if annual volume (in thousands of pounds) is 50,200,350 and 500. Circle the lowest cost at each annual volume.

- Based only on annual cost, for what range of annual volumes would each option be preferred?

- What factors other than annual cost should be considered when making this decision?