Answer the following questions for each configuration in the table below. 

1. How many subnets?
2. How many hosts per subnet?
3. What are the valid subnets?
4. What are the valid hosts per subnet?
5. What is the broadcast address for each subnet?

|  | IP ADDRESS | SUBNET MASK |
| --- | --- | --- |
| CONFIGURATION A | 192.168.10.0 | 255.255.255.192 |
| CONFIGURATION B | 220.110.16.0 | 255.255.255.224 |
| CONFIGURATION C | 219.220.250.0 | 255.255.255.248 |