An automobile tire has a radius of 0.370 m, and its center moves forward with a linear speed of v = 16.0 m/s.

(a) Determine the angular speed of the wheel. (Assume that there is no slipping of the surfaces in contact during the rolling motion.)
rad/s

(b) Relative to the axle, what is the tangential speed of a point located 0.175 m from the axle?
m/s

Section 8.6 Rolling Motion

2. --/33.33 points No Response | Show Details Notes

| part | score | total |
| --- | --- | --- |
| 1 | -- | 33.33 |

A uniform plank of length 4.8 m and weight 227 N rests horizontally on two supports, with 1.1 m of the plank hanging over the right support (see the drawing). To what distance x can a person who weighs 449 N walk on the overhanging part of the plank before it just begins to tip?
m

3. --/33.34 points No Response | Show Details Notes

| part | score | total |
| --- | --- | --- |
| 1 | -- | 33.34 |

A CD has a mass of 17 g and a radius of 6.0 cm. When inserted into a player, the CD starts from rest and accelerates to an angular velocity of 18 rad/s in 0.84 s. Assuming the CD is a uniform solid disk, determine the net torque acting on it.
N·m