Given the Rician PDF

(3.23)

Probability of False Alarm

The probability of false alarm is equal to the area underneath  from the threshold to infinity, that is:

(3.24)

Similarly, the probability of detection is equal to the area under  from the threshold to infinity.  Unfortunately the integral of (3.23) can be expressed only by tabulated functions.  A simple approximation can be obtained, however when the SNR is high-that is, when

Signal to Noise Ratio

(3.26)

If the condition expressed in (3.26) is met, the PDF will have the sape of a sharp peak near r = A, which means that in the argument of the modified Bessel function we can replace rA with , and that this argument will be very large.  Using the approximation

(3.27)

yields, for large SNR

(3.28)