Q1. A pile of 500 sheets of paper has a mass of 2 kg. The pile is 300mm long, 200mm wide and 50 mm thick. Calculate

- the thickness of the sheet

- the mass of one sheet.

- The volume of the pile

- The density of the paper

- The mass of a one square metre sheet of this paper.

Q2 A plastic bag filled with air has a volume of 0.008m3. When the air in the bag is squeezed into the rigid container, the mass of the container (with air) increases from 0.02 to 0.03kg . Calculate the density of the air in the bag.

Q3 The density of air is 1.3 Kg/m3 . Calculate the loss in the mass of a 5 litre flask when the air inside the is removed by a vacuum pump.( 1 litre = 1000 cm3 or 1.0 X 10-3 m3)

Q4 How many ml are there in 1 m3?

Q5 How many cm3 are there in 1 m3?

Q6 density of following substances in g/cm3.

Copper 8.9

Iron 7.9

Kerosene 0.87

Mercury 13.6

Water 1.0

1cm3 of mercury has a greater mass than 1 cm3 of any other substance in this table

- True or False

1cm3 of water has a smaller mass than 1 cm3 of any other substance in this table

- True or False

1g of iron has a smaller volume than 1g of copper.

- True or false

1g of mercury has a greater mass than 1g of copper.

-  true or false

Q7 Explain hoe to take readings with vernier caliper if both the scales are in millimeters.

Pls provide explanation to all questions.