Problem 1:

A time study is performed on an operation, resulting in the data following (in minutes).

Cycle

| Element | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | Performance Rating |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1. Get and position unit | 0.22 | 0.27 | 0.19 | 0.24 | 0.17 | 0.24 | 0.21 | 0.18 | 1.10 |
| 2. Perform calibration | 2.20 | 2.70 | 2.50 | 3.10 | 2.80 | 2.40 | 3.20 | 2.70 | 1.30 |
| 3. Perform standard tests | 4.60 | 4.00 | 4.50 | 3.80 | 4.30 | 4.50 | 3.90 | 4.40 | 0.85 |
| 4. Update card and remove unit | 0.50 | 0.50 | 0.70 | 0.60 | 0.80 | 0.40 | 0.50 | 0.60 | 1.20 |

Allowance per Eight-Hour Shift:

Clothes change	15 minutes

Unavoidable delay	35 minutes

Lunch			30 minutes

Shower and change	30 minutes

Total			110 Minutes

- Compute the mean observed time for each element in minutes.

- Compute the normal time for each element and total normal time in minutes.

- Compute the allowance fraction for the operation. Assume 480 minutes per shift.

- Compute the labor standard for the operation.

Problem 2:

A work-sampling study was conducted of an assembly operation. The results of the study are:

| Activity | Number of Observations |
| --- | --- |
| Assemble products | 85% |
| Allowances | 15 |

If the workers who were performing the operation during the study each produced an average of 100 products per eight-hour shift and received a performance rating of 1.15, what is the labor standard per product?

Problem 3:

It takes a manufacturer 120 hours to produce the first product in a batch of 15 products, and a 75 percent learning rate is expected.

- Estimate the time it will take to produce the fourth product.

- Estimate the total time it will take to produce the entire batch