I copied the code present there (you need to slightly modify it for your solution)

Example G01

%                       (PROGRAM START FLAG)

:1002                   (PROGRAM #1002)

N5 G90 G20              (BLOCK #5, ABSOLUTE IN INCHES)

N10 M06 T3              (TOOL CHANGE TO TOOL #3)

// you can omit the above statement, (optional)

N15 M03 S1250           (SPINDLE ON CW AT 1250RPM)

// same with the above statement, since no information is given regarding the speed

// and feed, (its better to assume some value)

N20 G00 X1 Y1           (RAPID OVER TO X1, Y1)

// X1, Y1 = (2in + 0.8in), (2in + 0.5in)

N25 Z0.1                (RAPID DOWN TO Z0.1)

// just above the surface

N30 G01 Z-0.125 F5      (FEED DOWN TO Z-0.125 AT 5IPM)

// change -0.125 to -0.1 and since feed is not specified, leave it as it is.

N35 X3 Y2 F10           (FEED DIAGONALLY TO X3, Y2 AT 10IPM)

// X3, Y2 = (2in + 3.2in), (2in + 1.5in), leave the feed as it is

N40 G00 Z1              (RAPID UP TO Z1)

// Z1 = 2in

N45 X0 Y0               (RAPID OVER TO X0, Y0)

// starting point X0, Y0 = 0, 0; 2in left and 2in bottom of down left corner

N50 M05                 (SPINDLE OFF)

N55 M30                 (PROGRAM END)

the X#s, Y#s, Z#s can be substitued with the respective values from the figure.