- The failure rate (λ) of a device is 22 failures per million hours.  Two standby units are added to the system.  Determine the MTBF of the system.

- Calculate the reliability of a system consisting of one operating unit and one identical standby unit operating for a period of 200 hours.  The failure rate (λ) of each unit is 0.003 failure/hour and the failure sensing switch reliability is 1.0.

- A system consist of five subsystems with the following MTBF’s:

  - Subsystem A:  MTBF = 10,540 hours

  - Subsystem B:  MTBF = 16,220 hours

  - Subsystem C:  MTBF = 9,500 hours

  - Subsystem D:  MTBF = 12,100 hours

  - Subsystem E:  MTBF = 3,600 hours

The five subsystems are connected in series.  Determine the probability of survival for an operating period of 1,000 hrs.

- Ten components were tested for 500 hours, each within prescribed operating conditions.  Component 1 failed after 30 hours;  Component 2 failed after 85 hours; Component 3 failed after 220 hours; And component 4 failed after 435 hours.  Determine the overall composite failure rate (λ) for the system.

- Suppose that you have the following design data on an equipment item and that, based on this data, you may wish to accomplish a reliability prediction.  What is the predicted MTBF?

| Component | Quantity of Parts Used | Failure Rate (% 1,000hrs) |
| --- | --- | --- |
| A | 16 | 0.135 |
| B | 75 | 0.121 |
| C | 32 | 0.225 |
| D | 44 | 0.323 |
| E | 60 | 0.120 |
| F | 15 | 0.118 |
| G | 28 | 0.092 |