- Find the Laplace transform of .

- Find the Laplace transform of .

- Find the Laplace transform of .

- Find the inverse Laplace transform of .

- Find the inverse Laplace transform of .

- Find the inverse Laplace transform of .

- The voltage and current in the Laplace domain for a certain system is given by. Is this system best described as resistive, capacitive, or inductive?

- The voltage and current in the Laplace domain for a certain system is given by. Is this system best described as resistive, capacitive, or inductive?

9.   For a second order RLC circuit, in the s-domain. If, is the system damped? If so, how? Characterize the behavior of the system.

10. A resistor and inductor are connected in series with a voltage source. If H, find the total response of the current. Assume there is initially no current. Identify the transient solution.