6. Determine the bandwidth required to support the multiplexer output for 10 4-kHz analog voice signals.

11. Determine the bandwidth required to support the multiplexer output for 10-analog voice signals digitized using standard PCM and a TDM multiplexer with an overhead of 10%.  Assume a bandwidth efficiency of 2-bps/Hz.

15. One of the 193 bits in the DS-1/T-1 transmission format is used for frame synchronization.  Explain its use.