Please reference this figure for the question:

22. Assume that a statistical multiplexer is used in the communications network described in Figure 1.  There are 20 sources that transmit 20% of the time at rate of 32kbps.

a. 	Can this system work if the QPSK modulation is used and the media will support a baud/symbol rate of 40 kbps?  Explain.

b. 	Can this system work if the baud/symbol rate is increased to 80kbps?  Explain.

c. 	If Part b can be supported, what will be the buffer size of the multiplexer?