Consider the transfer of a file containing one million 8-bit characters from one station to another.  What is the total elapsed time and effective throughput for the a bus topology with two stations a distance D apart, a data rate of B bps, and a packet size P with 80 bits of overhead.  Each packet is acknowledged with an 88-bit packet before the next is sent.  The propagation speed on the bus is 200 m/us.  

Solve for:

1. D= 1km, B = 1Mbps, P = 256 bits

2. D= 1km, B = 10Mbps, P = 256 bits

3. D= 10km, B = 1Mbps, P = 256 bits

4. D= 1km, B = 50Mbps, P = 10,000 bits