| Rule | Explanation | Percentage of Power Lost/Gained | Current Power Level | Example |
| --- | --- | --- | --- | --- |
| -3 dB | Half the watt value | 50% lost | Half of original | 100 mW – 3dB = 50 mW |
| +3 dB | Double the watt value | 100% gained | Double the original | 10 mW + 3dB = 20 mW |
| -10 dB | Decrease watt value to one tenth of original | 90% lost | One-tenth of original | 300 mW -10 dB = 30 mW |
| +10 dB | Increase the watt value by ten-fold | 1,000% gained | Ten times the original | 10 mW = 10 dB = 100 mW |