A factory’s electrical load can be represented as three parallel admittances (see attachment). The values of the admittances are given in the table in polar form.

- Determine

  - The current taken from the supply

  - The overall power factor of the load

  - The value of the capacitor required in parallel to the load to reduce the supply current by 20% and the new power factor with the capacitor in circuit

- The power factor for the factory load can be improved to unity by using a sufficiently large parallel capacitor

  - Calculate the value of this capacitor

  - Calculate the resonant frequency of the circuit when this capacitor is in circuit (using the condition that at resonance BC = BL, like XC = XL in a series circuit). Please comment on this answer.

  - State, with reasons, if the ‘unity power factor’ condition gives the minimum value of supply current.