LAB #7 clothes dryer

Inputs:

1)      door switch

2)      Start button

3)      Stop button

4)      Clothes sensor switch

Outputs:

1)      Cycle complete buzzer

2)      Low heat Light

3)      High heat  Light

4)      Door open Light

Rules of operation:

1.       Clothes dryer door open, the Door open light comes on.

2.        Dryer will not work if there are no clothes in the dryer.

3.       The dryer cycle can only start when the start button is pressed.

4.       There are only 2 ways the cycle will stop once its has started. The 2 ways are by opening  the door, and pressing the stop button.

5.       Once the dryer starts, the low heat cycle works for 12seconds. Immediately after the low heat cycle is complete the high heat cycle begins and stays on for 14 seconds.

6.       Once the high heat cycle is complete the cycle complete buzzer will light up.

7.        If the dryer is stopped it must start at the beginning of the low heat cycle.

Labs must be handed in showing  Logosoft program, digital circuit and final LogoSoft program