1. For a discrete-time signal x[n] with the z-Transform: X(z) = z 8z2-2z-1 find the z-Transform, V(z) for the signal v[n] = e3nx[n]. 2. Compute the z-Transform for the discrete-time signal x[n] = (0.5)nnu[n]. 3. A linear time-invariant discrete-time system is excited by the input x[n] = δ[n] + 2u[n-1]. The resulting output response with zero initial conditions is y[n]=(0.5)nu[n]. Determine the transfer function of the system.