1.

The midrange open gain of a certain op-amp is 100,000. If the open loop critical frequency is 75 Hz, what is the open loop gain at 1 KHz?

2.

A certain op-amp has three internal amplifier stages with the following gains and critical frequencies: A1 = 50 dB at f1 = 1000Hz, A2 = 70 dB at f2 = 100Hz, A3 = 30 dB at f3 = 25,000Hz. Determine the open loop midrange dB gain.

3.

For the op-amp in problem 2, determine the phase lag when f = f1.

4.

The op-amp in figure 1 has a unity-gain bandwidth of 3 MHz and the RF = Find the bandwidth.(100Kohms and Ri = 5Kohms.  Please note that these figures will be used for the remainder of the exam questions.

5.

The op-amp in figure 2 has a unity-gain bandwidth of 3 MHz and the RF = Find the bandwidth.(200Kohms and Ri = 4Kohms

6.

Using figure 3 find the output voltage if the 3 input voltages are 1V, 2V, and 3V (starting with the top resistor and going down) and RF = 15Kohms

7.

Using figure 3 with RF = 15 kohms and 3 input voltages are 1V, 2V, and 3V (starting with the top resistor and going down) find the current through RF.

8.

A low pass filter has a critical frequency of 1kHz. What is its bandwidth?

9.

A high pass filter has a R = 3kohms and C = 0.0020microF. What is its critical frequency?

10.

What is the roll-off rate of a 3rd order low pass filter?