Question 3

Fig. Q3 shows a rigid light beam which is hinged at O to a wall. The beam carries a point mass of m at the free end. The beam is connected at its mid-point to a spring (stiffness k) which is also connected to a support that moves with a vertical motion y = Y sin(t. A damper (coefficient c) connects the mid-point of the beam to a fixed support.

(i)	By taking moments about O of the forces acting on the beam show that an equation of motion can be obtained with the form

4

where x is the displacement of the mid-point of the beam. 	         [8 marks]

(ii)	Determine the maximum value for ( if the amplitude ratio of the x 			displacement  (i.e. X)  to Y is not to exceed 10%.

Take m =  2 kg;   k = 6.25 kN/m;  c = 45 Ns/m. 		        [12 marks]

(Answer:  87.8 rad/s)

Fig. Q3

# Text boxes

O