Top of Form

Maximum number of choices allowed is {0}.

Javascript not enabled

Your browser does either not support Javascript or has Javascript disabled. This assessment contains features that requires Javascript. Refer to your browser's documentation to determine if Javascript is disabled and how to enable it. If you are using a browser that does not support Javascript switch to a different browser.

5. Determine the Laplace transform of ƒ(t) = + 5e-4t + 12sin 3t. A) B) C) D) 6. Find the inverse Laplace transform of . A) B) C) D) 7. If v(t) = 10e-t/3 for some circuit, when does the voltage fall to 37% of its initial value? A) 1/3 seconds B) 30 ms C) 300 ms D) 3 seconds 8. If the voltage initially across a 2 F capacitor is zero, what is the instantaneous power if the current is A? A) p = 3/10(1 − e-2t) W B) p = (8/3)e-3t − (2/3)e-3t W C) p = (8/3)e-3t − (2/3)e-6t W D) 0 W 9. Let ƒ(t) = sin2t. What is the Laplace transform of dƒ / dt ? A) B) C) D) 10. The charge in a certain capacitor varies as q = 20e-4t sin 2t C. What is the voltage if the capacitor is 2 F? A) v = 10e-4t sin 2t V B) v = -40e-4t sin 2t V C) v = 400e-4t sin 2t V D) v = 40e-4t cos 2t V 11. The charge in a certain inductor varies as q = 2 sin 2t C. What is the voltage if the inductance is 2 H? A) v = 10 sin 2t V B) v = -4 sin 2t V C) v = 4 cos 2t V D) v = -16 sin 2t V 12. The current flowing through a 1 H inductor is 10 cos 20t amps. Find the voltage. A) 10 cos 20t volts B) 200 cos 20t volts C) 200 sin 20t volts D) -200 sin 20t volts 13. The current flowing through a 2 F capacitor is i(t) = 5 cos 2t amps. What is the voltage? A) 5 + 5/4 (sin 2t) V B) -5 cos 2t V C) -10 sin 2t V D) 0 V 14. The current flowing through a 2 H inductor is i(t) = 5 cos 2t amps. What is the voltage? A) 5 + 5/4 (sin 2t) V B) -5 cos 2t V C) -20 sin 2t V D) 0 V 15. The current flowing through a 5 F capacitor is i = 3e-2t. What is the voltage as a function of time, if the initial voltage is zero? A) v = 3/10 (1 − e-2t) B) v = 3/10 (1 + e-2t) C) v = -30e-2t D) v = -6e-2t 16. The current through an inductor is . What are the zeros? A) Zero at s = 0 B) None C) Zeros at s = -1, -3 D) One zero at s = -1 17. The voltage across a 2 F capacitor is v = 20e-4t volts. What is the instantaneous power? A) p = 1600e-8t W B) p = -1600e-4t W C) p = -1600e-8t W D) 0 18. What are the zeros and poles of ? A) zero: -1/2; poles, -3,-1 B) zeros: -3,-1; poles: -1/2 C) No zeros; poles -3,-1 D) Poles: -1/2,-3,-1 19. What is the energy in a 2 F capacitor if v(t) = cos2t at t = π seconds? A) 24 joules B) 1 joule C) 1 W D) 4 joules 20. What is the energy in a 10 H inductor if i(t) = cos2t at t = π seconds? A) 5 joules B) 1 joule C) 1 W D) 4 joules 21. What is the impedance of a 4 F capacitor? A) 4 B) 4/s C) 1/4s D) 1/s 22. What is the Laplace transform of 2u(t)? A) 1/2 B) 1/2s C) 2/s D) 1/s 23. What is the Laplace transform of e-2t sin t ? A) B) C) D) 25. What kind of damping is associated with ƒ (t) =(A + Bt) eωt? A) Underdamping. B) Critically damped. C) Critically underdamped. D) Overdamped.

| Assessment: |  |
| --- | --- |
| Question Set: |  |

Bottom of Form

## Answers Saved

Your answers will be saved, but the assessment will not be submitted. 

Click Ok to finish the assessment later or Cancel to continue taking the assessment.

## Error

The following error occurred:

## Error

The following error occurred while submitting your answers:

Please correct the problem and try submitting again.

## Time expired

Your time has expired. Submit the assessment now or you may be penalized.

Your time has expired. The assessment will be automatically submitted.

## Time warning

You have  minute(s) remaining.

## Time expired

Your time for this question set has expired. Proceed to the next question set or submit the assessment now or you may be penalized.

Your time for this question set has expired. You will automatically move to the next question set.

Your time for the last question set has expired. The assessment will be automatically submitted.

## Time warning

You have  minute(s) remaining for this question set.

## Incomplete Submission

You did not answer the following questions:

Click Ok to submit the assessment or cancel to answer these questions.

## Incomplete Submission

You did not answer the following questions:

Click Ok to answer these questions.

## Upload files