The circuit is used to measure the internal impedance of a battery.

The battery being tested as a NiMH battery cell.

A fresh battery is being tested, and it is found that the voltage Vout,

is 2.28 V with the switch open and 2.27 V with the switch closed.

Find the internal resistance of the battery.

# Text boxes

Rb

Switch

10 ohms

+

-

Vout