1)

If  a charge of 8uC is at the top of the y-axis and  -1.2uC is at the origin. The distance between the is 3cm. a third charge 7uC is on the x-axis. The distance between the second and third charge is 4cm. find

- the electric field at the center of the triangle.

- The electric potential at the center of the triangle.

- The energy required to assemble the configuration of the charges in the triangle.

- A parallel plate capacitor is formed of  two 10cmX10cm plates spaced 1cm apart. The plates are charged to +/- 1nC. An electron is shot through a very small hole in the positive plate. What is the slowest speed the electron can have if it is to reach the negative plate.

- A 100mg pith ball hangs by a thread in the center of a parallel plate capacitor. The capacitor plates are 5cm X 5cm and spaced 1cm apart. When the ball is charged to +10nC and the capacitor plates are charged to +/-Q, the ball hangs at a 3degree angle. What is Q?

- A 6V and 3V battery is connected to a circuit with two parallel resistors of 6 and 12 ohms. How much power is dissipated by the 12 ohms resistor. What is the value of the potential at the four edges of the circuit.