Problem:

A saturated liquid mixture containing 60 mole % benzene and 40 mole % toluene is to be distilled continuously into a distillate product containing 90 mole % benzene and the bottom product containing 5 mole % benzene. The fractional distillation column will operate at approximately constant pressure of 1 atm. The reflux ratio is 2. How many theoretical plates must the column have if the feed is introduced into the eighth plate? Equilibrium data are:

| x | 0 | 0.017 | 0.075 | 0.13 | 0.211 | 0.288 | 0.37 | 0.411 | 0.581 | 0.78 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| y | 0 | 0.039 | 0.161 | 0.261 | 0.393 | 0.496 | 0.591 | 0.632 | 0.777 | 0.9 | 1 |