Problem:

Vapor pressures of chlorobenzene and water are given below:

| Pressure, mm Hg | 100 | 50 | 30 | 26 |
| --- | --- | --- | --- | --- |
| Temperature oC, Chlorobenzene | 70.4 | 53.7 | 42.7 | 34.5 |
| Temperature oC, Water | 51.7 | 38.5 | 29.9 | 22.5 |

If steam is blown into the still containing a mixture of these two components and the total pressure is 130 mm Hg, estimate the temperature of boiling and the composition of the distillate. The two components are immiscible in the liquid