1

|  |  | The slender bar with a mass of 4 kg is released from rest at an angle of 35 degrees. What is the angular velocity of the bar when it is vertical? a. 0.667 rad/s b. 1.06 rad/s c. 0.888 rad/s d. 1.74 rad/s e. 2.31 rad/s |
| --- | --- | --- |

2

|  |  | The stepped disk weighs 50 lb and its mass moment of inertia about its center is I = 0.4 slug-ft2. If it is released from rest, determine its angular velocity when it falls 3 ft. The rope does not stretch. a. 22.9 rad/s b. 10.2 rad/s c. 8.20 rad/s d. 32.2 rad/s e. 15.7 rad/s |
| --- | --- | --- |

3

|  |  | An assembly consists of two 15-lb slender rods and a 20-lb disk. The spring is unstretched when  = 45o and the assembly is released from rest at this position. The disk rolls without slipping. Determine the angular velocity of rod AB at the instant  = 0. a. 3.89 rad/s b. 3.65 rad/s c. 3.12 rad/s d. 2.69 rad/s e. 4.28 rad/s |
| --- | --- | --- |