Problem:

1000 kg/hr of a mixture containing 42 mole percent heptane and 58 mole percent ethyl benzene is to be fractionated to a distillate containing 97 mole percent heptane and a residue containing 99 mole percent ethyl benzene using a total condenser and feed at its saturated liquid condition. The enthalpy-concentration data for the heptane-ethyl benzene at 1 atm pressure are as follows:

| xheptane | 0 | 0.08 | 0.18 | 0.25 | 0.49 | 0.65 | 0.79 | 0.91 | 1.0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| yheptane | 0 | 0.28 | 0.43 | 0.51 | 0.73 | 0.83 | 0.90 | 0.96 | 1.0 |
| Hl (kJ/kmol) x 10-3 | 24.3 | 24.1 | 23.2 | 22.8 | 22.05 | 21.75 | 21.7 | 21.6 | 21.4 |
| Hv (kJ/kmol) x 10-3 | 61.2 | 59.6 | 58.5 | 58.1 | 56.5 | 55.2 | 54.4 | 53.8 | 53.3 |

Calculate the following:

- Minimum reflux ratio

- Minimum number of stages at total reflux

- Number of stages at reflux ratio of 2.5

- Condenser duty

- Reboiler duty