Problem:

Develop the overall rate equation for the gas-phase heterogeneous reaction A  M + N, considering the following steps:

- adsorption of A,

- surface reaction between the adsorbed A and adjacent site to produce adsorbed M and adsorbed N, and

- desorption of M and N

Assume step (ii) is controlling.