# Question 1

A hollow shaft 105mm outside diameter, 85mm inside diameter is subjected to a maximum bending moment of 4 kN-m. If the yield stress of the material is 400MPa, calculate the maximum torque which can be applied under these conditions assuming a safety factor of 3 and the Tresca failure criterion.

## Question 3

A component is subjected to loading conditions which result in the following stress conditions at a point on the surface, (x = -40MPa,  (y = 50MPa and (xy = 35 MPa.

### Determine :-

- the magnitude and orientation of the principal stresses

- the magnitude and orientation of the maximum shear stress

- the stresses acting on  a plane whose normal makes angle of 30( clockwise from the x-axis.

## Question 5

An 80mm diameter transmission shaft projects 300mm from a bearing housing. The shaft is subjected to a torque of 7 kN.m and a vertical cantilever load of 10 kN at the end of the shaft.

- Show, by means of a sketch, the critical positions on the surface of the shaft, where the maximum stresses occur.

- Determine the principal stresses at the critical positions.

- If the yield stress of the material in simple tension is 280 MPa, determine the Factor of Safety according to:

- the Tresca yield criterion and

b)   the Von Mises yield criterion.

## Question 6

A rectangular beam, cross section 60mm x 110mm as shown in Fig. Q3, is subjected to a bending moment of 35 kN.m about the horizontal axis a-a.

Determine the thickness of the elastic core x assuming the material is elastic perfectly plastic with a yield strength of 240MPa.

#### Fig. Q3

# Text boxes

x

aa

aa

110mm

60mm