1)

Figure 1 represents the equivalent circuit of a voltage regulator where an unregulated 12V source is used to provide a stabilised voltage Vout using an 8V zener diode.

Using Kirchhoff’s voltage law and by writing the appropriate equations find:

i.	The currents   i2 & i3.

ii.	The output voltage Vout.

iii.	The power dissipated by the zener diode (resistor RZ).

2)

a p.d. of  V  is connected between terminals A and B of  the network below-

For a frequency of 32.274861 kHz calculate :

a. 	The j notation impedance of the network.

b. 	The polar representation of the impedance in the form  giving the answer as a positive angle.

c. 	The magnitude of the voltage across C2 and its phase relative to the supply voltage.

# Text boxes

i2

i3

i1

RZ

R2

0.5 

500 

8 V

100 

12 V

C

D

B

Figure 1

R1

10 

A

R3

VZ

Vout

A

B

C1

120 pF

8 µH

L

R = 14 

C2

10 nF

Figure 2