Audio products inc produces two AM/FM/CD players for cars.  The radio/CD units are identical but the mounting hardware and finish trim differ.  The standard model fits intermediate and full size cars, and the sports model fits small sports cars.

Audio Products handles the production in the following way.  The chassis (radio/CD unit) is assembled in mexico and has a manufacturing lead time of two weeks.  The mounting hardware is purchased from a sheet steel company and has a three week lead time.  The finish trim is purchased from a Taiwan electronics company with offices in los angeles as prepackaged units consisting of knobs and various trim pieces.  Trim packages have a two week lead time.  Final assembly time may be disregarded because adding the trim package and mounting are performed by the consumer.

Audio products supplies wholesalers and retailers, who place specific orders for both models up to eight weeks in advance.  These orders, together with enough additional units to satisfy the small number of individual tastes, are summarized in the following demand schedule.

Week

| Model | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Standard Model |  |  |  | 300 |  |  |  | 400 |
| Sports Model |  |  |  |  | 200 |  |  | 100 |

There are 50 Radio/CD units on hand but no trim packages or mounting hardware.

Prepare a material requirements plan to meet the demand schedule exactly.  Specify the gross and net requirements, on hand amounts, and the planned order release and receipt periods for the radio/cd chassis, the standard trim and sports care model trim, and the standard mounting hardware and the sports car mounting hardware.