Refer to diagram

1.Derive an algebraic expression for the transfer function of the circuit assuming that no external load is connected between terminals A&B. Simplify the expression as far as possible but do not attempt to rationalise it. Refer to the two reactances as Xc & Xl.

2. Calculate voltages V & Vout in polar form and draw a phasor diagram showing these voltages together with the source voltage phasor.

# Text boxes

C

A

B

R2

L

R1

V

Vout

500Ω

2kΩ

20nF

25mH

10 Vrms

50kHz