4) In the following circuit, what is the current through R1 at T=1 second after 
the switch is closed? How long does it take the capacitor to be 95% fully 
charged?

# Text boxes

R1=2Momga

V=15V

C=2uF

R2=6Momga