Refer to diagram above

1. Derive an expression for the complex impedance between terminals A&B referring  to the reactances as Xc & XL. Express the answer in the form of (real part + j * imaginary part)

2. Calculate the phase angle of the current I relative to the voltage Vin for a source frequency of 3kHz(must be done using the simplest form possiable for calculation).

3. Describe two ways in which the circuit could be changed to make it resonate at a frequency of 3kHz. State exactly how you would make any necessary calculations (do not attempt to do these calculations)

# Text boxes

A

B

C

50nF

I

R1

10kΩ

R2

5kΩ

L

100mH

10kΩ

Vin