%Tossing a lead weight: example of linear regression error from BME221 lecture

%matrix of modeling functions: first column of ones, second column = t,

%third column = -0.5*t^2 (data is modeled by h = h0 +V0*t +0.5g*t^2).

%We shall denote our model by the vector equation A*x=b

A=[ones(1,5);0:4;-0.5*(0:4).^2]'

%height measurements in meters

h=[0.3 14.8 20.7 15.9 2]'

K=inv(A'*A)*A'

% our modeling parameters, (h0,V0,g)

x=K*h

%variance in data

Shsq=sum((h-A*x).^2)/(5-3)

%variance in first modeling parameter, for demonstration only.

%other variances and covariances can be extracted from the symmetric SIGMAxsq.

Sx1sq=K(1,:)*K(1,:)'*Shsq

%SIGMAbsq: matrix of covariance of the observations b.

%If the observations are independent then SIGMAbsq will be diagonal only.

%We further assume that all observations have the same variance.

%(a common assumption)

SIGMAbsq=eye(5)*Shsq

%matrix of covariance of the regression parameters

SIGMAxsq=K*SIGMAbsq*K'

%Suppose we wish to determine the model value at 100 points ranging from 0 to 4.

%Thus, we now have the vector equation: bm = Am*x

Am=[ones(1,100);linspace(0,4,100);-0.5*linspace(0,4,100).^2]';

%Finally, we have the matrix of covariance of bm.

%In general, only the diagonal elements of SIGMAbmsq are of interest.

sigmabmsq=diag(Am*SIGMAxsq*Am');

plot(A(:,2),h,'o',Am(:,2),Am*x)

hold on

plot(Am(:,2),Am*x+sqrt(sigmabmsq),'r--',Am(:,2),Am*x-sqrt(sigmabmsq),'r--')

hold off

legend('data','best-fit model','69% confidence (1\sigma) interval')

xlabel('t  (sec)')

ylabel('h  (m)')