9

For the circuit shown below, find the values for Re and Rc to establish a collector current of 0.6 mA and a reverse-bias voltage on the collector-base junction of 2.2 V. Assume alpha is approximately equal to 1. Rc = 6.33 k, Re = 5.1 k Rc = 6.1 k, Re = 5.3 k Rc = 6.1 k, Re = 5.5 k Rc = 6.33 k, Re = 5.5 k